## Slide 1
REALTIME DENSITY SENSOR

## Slide 2
Real-Time Density Sensor
Using radio technology to predict tailings density, this system provides real-time data, improving process control and optimising material handling.
JULY 2020
JULY 2022
JULY 2023
  REALTIME DENSITY SENSOR

## Slide 3
DATA SOURCES
  WHAT WE HAVE ACHIEVED
The Realtime Density Sensor was deployed in Mount Weld, Laverton (Rare Earths).
The results are a combination of two parts:
Collected values from Density Sensor every 10 seconds
Collected values from Shear Vanes samples every 10 minutes
Very Soft
Soft
Firm
Medium
1000mm ↓
THE DEEPER WE GO, THE LOWER THE RESOLUTION OF THE PREDICTABILITY

## Slide 4
DATA SOURCES
  SO, WHAT HAS CHANGED?
+300mm
LESSONS LEARNED!
Material
Heat
Height

## Slide 5
DATA SOURCES
  PHYSICAL DESIGN IMPROVEMENTS
Mount / Frame material: 10.0mm Alu 5083 Grade, Black Anodised finish
Mounting location change: from Jacking Legs to front of Chassis
Cover assembly: 3D print or plastic mould … TBD
Cover Assembly change: Splash Guard to prevent material from entering cavity (not currently displayed)

## Slide 6
DATA SOURCES
  BILL OF MATERIALS
Mount / Frame: $800
VNA: $5,000
Onboard Computer: $100
Computer Housing: $20
Actuator: $420
Internal Cables: $100
Vivaldi Antenna: $120
Frame Ancillaries: ~$400
Cover Assembly: ~$500
Harness: ~$500
Assembly: Inhouse
$7960
+ Assembly
+ Installation
+ Commissioning

## Slide 7
DATA SOURCES
  HOW ARE WE PROGRESSING?

## Slide 8
  DELAYED: WHEN & WHY
JULY 2020
JULY 2022
JULY 2023
Data collecting & Preprocessing
Data Integration
Machine Learning
JULY 2025
WE HAVE CHANGED THE WAY THE WE COLLECT DATA
WE HAVE RESEARCHED AND
TESTED ACROSS VARIOUS MACHINE LEARNING MODELS
WE HAVE INCREASED OUR UNDERSTANDING OF DATA INTEGRTION

## Slide 9
  A GLIMPSE INTO THE FUTURE
Extended research has been conducted to seek a correlation / validation means to tie MudMaster performance into the Density Sensor prediction model.
These values include:
Engine Torque
Scroll Traction
GPS Speed
Traction Difference
Sentinel-2 Satellite
Worsley
2025/01/27
SATELLITE-BASED MOISTURE IMAGERY
MudMaster MoTeC
Worsley
2025/01/27
MOTEC DRIVEN - POWERBI REPORTING

## Slide 12
USB Mini B
USB-B
USB-A
-
+
USB-A
2 in 1 out
USB Hub (Targus ACH214)
USB-B
Into Arduino PC
12v Connector block to in-cab Fuse
Bare wire into Arduino Power/In and Power/Out
USB-B Plug in
-
+
500mm
500mm
500mm
500mm
500mm
~10m USB-A Male (in cab) to USB-A Female (Antenna)
~10m 12v cable (at Fuse block to the Antenna)